## Slide 1
G19
01
DIGITAL ASSIGNMENT II
ML-Based Pre-Screening
and Verification Referral
for Hotspots
Lithography hotspot detection on ICCAD-12 benchmarks
AI and Machine Learning for IC
BEVD402L Group G19 Fall 2026-27
Notes: Project title, course, group and semester: DA2_BVD_AIML_4.9.2026.pdf, pages 1 and 5. The presentation summarizes supplied project scripts and saved outputs.

## Slide 2
Group G19 and course details
G19
02
Group member | Registration number
BONTHALA SAI KIRAN | 24BVD1106
BANDA SIRICHANDANA | 24BVD1114
KAMAL SHARMA | 24BVD1118
KARTHIKEYAN R V | 24BVD1119
Faculty
Dr. G. Lakshmi Priya
Class slot
D1+TD1
AI and Machine Learning for IC
Course code: BEVD402L
Programme: B.Tech. (BVD) Semester: Fall 2026-27
Notes: Source: DA2_BVD_AIML_4.9.2026.pdf, page 1 for course details, page 5 for G19 allocation. Four names appear in the G19 group allocation, despite the generic cover statement of a three-student group. All four listed members are retained. Class number: CH2026270102565. Assignment submission date: 20/09/2026.

## Slide 3
Research problem and objective
G19
03
Lithography hotspots
Sensitive layout patterns can print as open circuits or short circuits.
Verification workload
Detailed simulation is computationally demanding. ML scores can help decide which patterns need further attention.
Research question
Can confidence-based referral reduce the hotspots passed unchecked while limiting verification workload?
Hotspot examples from the reference paper
Notes: Background and figure: Ajay Verma, K Akhilesh Rao and Dhruva S Hegde, Lithography Hotspot Detection using Deep Learning, supplied Reference Paper.pdf, page 1, Figure 1. Research question adapted to the G19 statement in DA2_BVD_AIML_4.9.2026.pdf, page 10.

## Slide 4
Reference work and project contribution
G19
04
Reference work
The supplied paper compares VGG16 features with classical classifiers against a CNN trained from scratch.
95.3%
Average validation balanced accuracy
of the paper’s custom CNN
Our implemented extension
A separate small CNN produces a hotspot score for each pattern. A decision layer screens, flags or refers the pattern.
Controlled comparison
The same test scores support the 0.50 baseline and all three referral threshold settings.
The paper’s validation result and our test results use different models and protocols, so they are contextual references.
Notes: Reference result: Reference Paper.pdf, page 3, section V.B. The paper uses a 12,873-parameter CNN with ELU blocks and Nadam. Our supplied baseline uses two ReLU convolution blocks, Adam and a dense layer, so it is a separate implementation rather than an exact reproduction. Local sources: C:/Users/kamal/Downloads/aiml_project_output/01_baseline_model.py and 02_referral_logic.py.

## Slide 5
Dataset and evaluation protocol
Five separate ICCAD-12 benchmarks. Counts below describe the saved test predictions.
G19
05
Benchmark | Hotspots | Non-hotspots | Test patterns | Hotspot share
B1 | 226 | 4,679 | 4,905 | 4.61%
B2 | 498 | 41,298 | 41,796 | 1.19%
B3 | 1,808 | 46,333 | 48,141 | 3.76%
B4 | 177 | 31,890 | 32,067 | 0.55%
B5 | 41 | 19,327 | 19,368 | 0.21%
146,277 test patterns
Hotspots: 2,750 (1.88% of test patterns)
Per benchmark: 15% of the training folder forms validation data. The supplied test folder remains separate.
Notes: Counts recalculated directly from predictions_benchmark_1.csv through predictions_benchmark_5.csv and checked against baseline_metrics_summary.csv. Total counts are descriptive only, and the primary experiments remain separate. Training protocol in 01_baseline_model.py: grayscale, 64 x 64 pixels, normalization by 255, validation_split=0.15 and split seed 42. Source training image folders were not included, so their class counts are not presented.

## Slide 6
CNN baseline and training setup
G19
06
Stage | Configuration
Input | 64 × 64 grayscale, pixel values scaled to 0–1
Feature extraction | Conv 16, 3 × 3, ReLU, batch norm, max pooling
Feature extraction | Conv 32, 3 × 3, ReLU, batch norm, max pooling
Classifier | Flatten, dropout 0.30, dense 64, sigmoid output
Training
Adam optimizer, binary cross-entropy, batch size 32, 10 epochs.
Class weights compensate for unequal training class frequencies.
Scores are oriented so that a larger value consistently indicates greater hotspot confidence.
Notes: Source: C:/Users/kamal/Downloads/aiml_project_output/01_baseline_model.py. Class weights equal total/(2 x class_count), calculated from the training subset. The loader determines the hotspot class index and flips sigmoid values when required, independently aligning test labels. Baseline prediction rule: score >= 0.50 means hotspot. The displayed settings come from the supplied implementation, and no retraining was performed for this presentation.

## Slide 7
Confidence-based screening and referral
Featured threshold pair: lower bound 0.20 and upper bound 0.80
G19
07
Hotspot score C | Code label | Decision
C ≤ 0.20 | safe | Screen out as likely non-hotspot
0.20 < C < 0.80 | needs_check | Refer for detailed verification
C ≥ 0.80 | risky | Flag as likely hotspot
A wider uncertainty interval produces more referrals
Thresholds 0.10/0.90 refer more cases than 0.30/0.70.
Notes: Source: C:/Users/kamal/Downloads/aiml_project_output/02_referral_logic.py and saved referral_labels_benchmark_* files. The executable bucket_label function and actual outputs define the behavior. Comments beside the threshold list reverse the wide/narrow interval interpretation, so this presentation uses the actual inequalities. The code label safe is a screening decision, not a guarantee that no hotspot exists. The project generates referrals but does not execute a lithography simulator or measure subsequent verifier accuracy.

## Slide 8
Baseline performance at the 0.50 cutoff
All values are percentages. Macro average gives each benchmark equal weight.
G19
08
Benchmark | Balanced accuracy | Precision | Recall | Specificity | F1-score
B1 | 75.02 | 45.63 | 53.10 | 96.94 | 49.08
B2 | 98.74 | 38.49 | 99.40 | 98.08 | 55.49
B3 | 96.53 | 43.85 | 97.95 | 95.11 | 60.58
B4 | 96.62 | 12.08 | 97.18 | 96.07 | 21.49
B5 | 93.59 | 3.45 | 92.68 | 94.51 | 6.66
Macro avg. | 92.10 | 28.70 | 88.06 | 96.14 | 38.66
Balanced accuracy = (recall + specificity) / 2. B1 has the lowest recall, while B5 has very low precision.
Notes: Source: baseline_metrics_summary.csv, verified against all five saved prediction files. Precision = TP/(TP+FP). Recall = TP/(TP+FN). Specificity = TN/(TN+FP). F1 = 2TP/(2TP+FP+FN). Balanced accuracy averages recall and specificity. The macro mean is the mean of five per-benchmark metrics, not a metric calculated from pooled counts. Overall accuracy is not used as the headline because the test sets are highly imbalanced.

## Slide 9
Baseline confusion counts
Hotspot is the positive class. Each row contains the four cells of a binary confusion matrix.
G19
09
Benchmark | True positive | False positive | False negative | True negative
B1 | 120 | 143 | 106 | 4,536
B2 | 495 | 791 | 3 | 40,507
B3 | 1,771 | 2,268 | 37 | 44,065
B4 | 172 | 1,252 | 5 | 30,638
B5 | 38 | 1,062 | 3 | 18,265
106 of 154 baseline misses occur in B1
This makes B1 the main source of missed hotspots in the supplied baseline results.
Notes: Source: baseline_metrics_summary.csv. All counts independently checked against the saved test labels and confidence values using the 0.50 threshold. The count 154 is the sum of five false-negative counts. This descriptive total does not replace per-benchmark evaluation.

## Slide 10
Fewer hotspots pass unchecked after referral
Featured thresholds: 0.20/0.80. Values show the share of real hotspots.
G19
10
Chart: 
| B1 | B2 | B3 | B4 | B5
Baseline missed hotspots | 0.46903 | 0.0060241 | 0.020465 | 0.028249 | 0.073171
Hotspots screened as safe | 0.16814 | 0.0040161 | 0.019358 | 0.022599 | 0.02439
11.94% baseline misses
4.77% screened-as-safe hotspots
Macro averages. The 7.17 percentage-point reduction measures routing changes. Verification outcomes are unmeasured.
Notes: Sources: predictions_benchmark_*.csv, baseline_metrics_summary.csv and referral_summary.csv. Baseline missed-hotspot rate = FN/(TP+FN), equivalently 1-recall. Referral missed-hotspot rate = true hotspots in the safe bucket / all true hotspots. The featured pair has mean referral rate 3.441684%. The reduction is 7.168588 percentage points. It does not demonstrate that a downstream verifier correctly recovers every referred hotspot.

## Slide 11
Threshold ablation and workload trade-off
Macro averages across five benchmarks. Routing shares use all patterns.
Unchecked-hotspot rates use true hotspots as the denominator.
G19
11
Low / high | Screened as safe | Flagged | Referred | HS passed unchecked
0.30 / 0.70 | 93.40% | 4.55% | 2.05% | 8.01%
0.20 / 0.80 | 92.43% | 4.13% | 3.44% | 4.77%
0.10 / 0.90 | 90.66% | 3.66% | 5.68% | 1.99%
0.10/0.90 has the lowest unchecked-hotspot rate tested
Its 1.99% unchecked-hotspot rate requires 5.68% referrals.
The 0.20/0.80 pair is the featured comparison, not a proven optimum.
Notes: Source: referral_summary.csv and overall_average_summary.csv. Values recalculated from the saved predictions. Macro averages: (0.3,0.7) referral 2.049373%, miss 8.009325%; (0.2,0.8) referral 3.441684%, miss 4.770104%; (0.1,0.9) referral 5.676510%, miss 1.991180%. No validation-based threshold optimization or external operating-cost constraint is documented.

## Slide 12
Screening decisions and verification workload
Routing shares at thresholds 0.20/0.80, as percentages of all test patterns
G19
12
Chart: 
| B1 | B2 | B3 | B4 | B5
Screened as safe | 0.86483 | 0.96351 | 0.9119 | 0.94973 | 0.93143
Referred | 0.1211 | 0.011245 | 0.0079142 | 0.012256 | 0.019568
Flagged | 0.014067 | 0.025242 | 0.080181 | 0.038014 | 0.048998
92.43% screened
3.44% referred
4.13% flagged
Macro averages. These routing shares indicate potential workload reduction. Runtime and simulation speed-up were not measured.
Notes: Source: referral_summary.csv, screening_efficiency_table.csv. Screening rate = n_safe/N, referral rate = n_needs_check/N, flagged rate = n_risky/N. The three mutually exclusive bucket rates sum to 100% per benchmark, apart from displayed rounding. The screened bucket still contains true hotspots. Work on flagged patterns also contributes to downstream workload. These fractions do not by themselves establish actual compute or time savings.

## Slide 13
Benchmark 1: what referral changes
Thresholds 0.20/0.80. The table shows true class versus routing decision.
G19
13
True class | Screened as safe | Referred | Flagged | Total
Hotspot | 38 | 136 | 52 | 226
Non-hotspot | 4,204 | 458 | 17 | 4,679
106 baseline misses
38 hotspots passed unchecked
Referral changes the routing of 68 baseline misses.
The verification queue contains 594 patterns, including 136 true hotspots.
Notes: Source: proposed_bucket_confusion.csv for benchmark 1 at thresholds 0.2/0.8, plus baseline_metrics_summary.csv. Baseline false negatives: 106. New safe-bucket hotspots: 38. Difference: 68 true hotspots with scores in (0.2,0.5) move from baseline negative decisions into needs_check. Verification queue: 136 HS + 458 NHS = 594 patterns (12.1101% of 4,905). A referred true hotspot is not a verified detection until the downstream check succeeds.

## Slide 14
Limitations and next steps
G19
14
Current evidence limit | Next step
No downstream verification results | Integrate a verifier and measure final detection metrics
No measured runtime or simulation cost | Benchmark inference and end-to-end verification time
No calibration or threshold selection study | Calibrate scores and choose thresholds on validation data
Single saved run per benchmark | Repeat runs and test sensitivity to random initialization
Persistent confident errors require model improvement
For B3, widening referral from 0.30/0.70 to 0.10/0.90 changes unchecked hotspots only from 36 to 34.
Notes: Evidence limits assessed from the supplied scripts and outputs: there is no simulator, verifier outcome log, timing output, calibration study, repeated-run summary or uncertainty interval. Proposed post-verification balanced accuracy, precision, recall and F1 therefore remain unknown. The G19 assignment brief also differentiates potential screening efficiency from demonstrated simulation speed-up.

## Slide 15
Conclusion
G19
15
The decision layer reduces the hotspots
that pass without further attention
7.17 pp
Lower macro unchecked-hotspot rate
at thresholds 0.20/0.80
3.44%
Macro share of patterns
referred for verification
The results support further evaluation of ML pre-screening.
Final detection reliability and runtime savings need verification evidence.
Notes: Conclusion based on verified per-benchmark test outputs. The selected headline pair is 0.20/0.80 as featured in 03_final_comparison.py. Macro baseline miss rate 11.938691%, macro safe-bucket miss rate 4.770104%, absolute difference 7.168588 percentage points. The base CNN is unchanged, and no downstream verifier outcomes were supplied.

## Slide 16
References and project materials
G19
16
Reference study
A. Verma, K. Akhilesh Rao and D. S. Hegde.
Lithography Hotspot Detection using Deep Learning.
IIT Bombay. Supplied reference paper, publication date not stated.
Assignment brief
Digital Assignment II, September 2026. AI and Machine Learning for IC,
BEVD402L. G19 project statement and group allocation.
Group project implementation and results
Baseline CNN, referral logic and final comparison scripts.
Saved models, test predictions and benchmark summary tables.
Notes: Source files: C:/Users/kamal/Downloads/Reference Paper.pdf; C:/Users/kamal/Downloads/DA2_BVD_AIML_4.9.2026.pdf; C:/Users/kamal/Downloads/aiml_project_output/01_baseline_model.py; C:/Users/kamal/Downloads/aiml_project_output/02_referral_logic.py; C:/Users/kamal/Downloads/aiml_project_output/03_final_comparison.py; C:/Users/kamal/Downloads/aiml_project_output/outputs/. Numerical evidence primarily uses predictions_benchmark_1.csv through predictions_benchmark_5.csv, baseline_metrics_summary.csv, referral_summary.csv and proposed_bucket_confusion.csv. Charts and tables in the presentation use editable native objects.